## Slide 1: The PBL, Part 3: KPP and TKE schemes
ATM 419/563
Spring 2024
Fovell
© Copyright 2024 Robert Fovell, Univ. at Albany, SUNY, rfovell@albany.edu
Notes: Removed exp 1 for 2023

## Slide 2: Outline
Some Richardson numbers
Recap of flux-gradient (1st-order) approach
Deficiencies of the flux-gradient approach
K-profile parameterization (KPP) schemes
TKE schemes
Notes: First order = everyone learns about it, but no one uses it. Not even such a scheme in WRF (until I added it for this class)

## Slide 3: Recall: Reynolds averaging
Divided variables into a mean (based on grid volume average over some time interval) and a deviation from it
The average was defined as:
And perturbations averaged out

## Slide 4: Richardson number(s)
A Richardson number (Ri) is a nondimensional measure of stability divided by shear (squared)
Named for NWP pioneer Lewis Fry Richardson
Some forms: gradient Ri, bulk Ri, surface bulk Ri, flux Ri
gradient Richardson number
bulk Richardson number
Notes: Bulk Ri approximates gradients discretized on a grid
Richardson forecast sfc p +145/6 h. Linear instability. Published 1922.

## Slide 5: Surface bulk Ri
A surface bulk Richardson number is computed from the surface up to height z, presuming wind speed at surface is zero.
Notes: Need to define TKE before defining flux Ri

## Slide 6: Turbulent kinetic energy
Turbulent kinetic energy (TKE) per unit mass can be defined as:
A prediction equation for averaged TKE* can be derived as
related to shear
related to vertical heat flux
dissipation/
other terms
Stensrud’s text, p. 169
*1D approximation already assumed
Notes: Shear (mechanical) generation of turbulence and convective (buoyancy) generation

## Slide 7: Flux Richardson number
related to shear
related to vertical heat flux
flux Richardson number
Normally negative (as winds
increase with height)
Negative when stable
Notes: Ri positive when stable because denom usually neg and numerator is neg when stable.

## Slide 8: Critical Richardson number (Ric)
When Ri ≤ Ric, turbulence can be produced. (However, preexisting turbulence is not necessarily extinguished when Ri rises above Ric.)
Ric is typically given as 0.25, but values used range between 0.0 and 1.0 (cf. Vickers and Mahrt 2004; Galperin et al. 2007; Hong 2010), with larger values often used when vertical resolution is poorer.
  e.g., Troen and Mahrt (1986) argued for using a relatively larger value.
More later…

## Slide 9: Ri, Ric and turbulence

## Slide 10
http://www.nzherald.co.nz/nz/news/article.cfm?c_id=1&objectid=11803687
K-H waves:
Shear-driven turbulence
Notes: Why eddies are important…

## Slide 11: K-H instability
Animation
High-resolution simulation. At lower resolution, you need to parameterize this!
Notes: Look at the MIXING the eddies accomplish. But you need HIGH RES to capture this effect. At lower res, you need to PARAMETERIZE it

## Slide 12: Explicitly resolved eddies, little extra parameterized mixing
∆x = 50 m

## Slide 13: No resolved eddies, considerable parameterized mixing
∆x = 500 m

## Slide 14: Review (1)
Eddies are not resolvable but important to the evolution of the PBL
We used Reynolds averaging to identify important eddy covariances such as:
We invoked flux-gradient theory to relate these covariances to eddy mixing coefficients acting on resolved-scale fields

## Slide 15: Review (2)
Then we used Prandtl’s mixing length theory to relate Km to mixing length lv and mean (absolute) shear S
Mixing length was presumed to be small near surface and grow (to some upper bound of 50-100 m or so) with height
We also discussed the log wind profile, how it must respond to stability, and saw mixing fields produced by 2 PBL schemes: YSU and MYJ in the in-class demonstration
Now: focus on a scheme that is just based on the equation above (a 1st-order scheme)

## Slide 16: 1st-order scheme
Computing Km from a mixing length and the base state vertical shear is called a 1st-order local closure scheme.
  “local” because Km only depends on local gradients
In original formulation, Km did not also depend on stability. The modified form modulates mixing by some function of stability: amplifying it when unstable, suppressing it where stable.
Blackadar (1979)
Notes: The f(Ri) is an improvement, but does not fix the scheme’s systemic problems

## Slide 17: A strongly-heated PBL (simulations with WRF SCM v.3.7.1)
Notes: Simulated using WRF SCM
This is using a higher wind initial sounding, and lower soil moisture, and that helps exaggerate diff wrt MRF

## Slide 18: A strongly-heated PBL
well-mixed
layer
superadiabatic
Notes: Remember how this was formed. The PBL top inversion is a consequence of the PBL mixing itself

## Slide 19: A strongly-heated PBL
well-mixed
layer
superadiabatic
Notes: Superadiabatic near sfc because mixing restricted near solid boundary. Mixed layer results owing to mixing through a deep layer.

## Slide 20: A strongly-heated PBL
well-mixed
layer
superadiabatic
11 radiosondes
31 days
Notes: Magnitudes, depths different, but shape is similar

## Slide 21: 1st-order scheme
well-mixed
layer
superadiabatic
First-order scheme’s
local mixing fails to
establish mixed layer
First-order
scheme
Notes: First order scheme fails to develop neutral mixed layer. Superadiabatic through a very deep layer.

## Slide 22: 1st-order scheme
Notes: “For statically unstable ABLs with vigorous convective thermals… wind speed becomes uniform with height a short distance above the ground.” – Stull’s Met for Sci and Eng, p. 81. If shear really disappeared, Km = 0 during time when it actually would be LARGEST. Indeed, shear is very small BECAUSE mixing is so large and effective.

## Slide 23: A fundamental inconsistency…
Eddy mixing Km helps remove vertical shear
Thus, as the shear S disappears, Km  0 in this equation
But, in reality, shear is smallest when mixing is most vigorous!
This model is too simple

## Slide 24: Einstein’s admonition
“Make things as simple as possible,
but no simpler.”
-- Albert Einstein
(1879-1955)
[attributed]
Wikipedia

## Slide 25: Beyond 1st-order schemes
KPP (K-profile parameterization)
[diagnosed mixing]
1.5-order scheme
[based on prognosed TKE e]
[S* is nondimensional
profile function]
ws = a velocity scale; h = PBL depth
Notes: Here 2022

## Slide 26: A strongly-heated PBL
Produced by
YSU (KPP) scheme
Notes: Simulated using WRF SCM

## Slide 27: A strongly-heated PBL
YSU and MYNN closer match
(YSU still “better”)
(MYNN has changed and added new features since WRF V3.7.1)
Notes: Those weren’t obs. They were the YSU solution, presumed to be closest to truth.
MYNN much closer to YSU in surface layer and lower half of mixed layer
(Should say MYNN2)

## Slide 28: K-profile parameterizations (KPP)
Including MRF, GFS, YSU, Shin-Hong

## Slide 29: KPP scheme lineage
Attempts to specify local mixing (i.e., mixing between neighboring model levels) with a certain and expected vertical distribution
Origins include: Brost and Wyngaard (1978) and Troen and Mahrt (1986)
MRF scheme developed for Medium Range Forecasting (MRF) model: Hong and Pan (1996). Still available in WRF!
  MRF/AVN models became GFS in 2002
MRF scheme evolved into GFS and YSU schemes
  GFS PBL scheme developed as MRF/AVN models became the GFS and was adopted for Hurricane WRF (HWRF). Continues in current HWRF model as the GFS-EDMF scheme and also in GFS-FV3.
  YSU scheme developed for WRF (Noh et al. 2003, Hong et al. 2006, Hong 2010)
  Shin-Hong (S-H) scheme evolved from YSU (Shin and Hong 2015)
  ACM2 (Pleim 2007) incorporates some aspects of KPP approach
Notes: Best citation abbreviation ever

## Slide 30: From PBL_Part2.pptx
Yamada and Mellor (1975)
Vertical profile at time
of maximum mixing
Mixing produced by a
TKE PBL scheme
KPP is trying to forge this

## Slide 31: A simple KPP scheme
p = 2 usually adopted
(but Brost and Wyngaard used p = 1.5)
MORE
• ws (velocity scale) = u*/fm
computed in surface layer*
(fm stability corrector, see Part 1)
• k = von Karman constant (~0.4)
Tasks:
• Determine PBL depth h
• Fit the profile to Km
Hong and Pan (1996)
*MRF/GFS velocity scale is constant with height. YSU’s is made a function of height.
Notes: MRF is simplest version of this approach – the basics
Unstable \phi_m < 1, amping up the velocity scale and thus the mixing

## Slide 32: A simple KPP scheme
Finding PBL top h
~ depends on selected critical Ri (Ric)
Compute surface bulk Ri (Ribs) for lowest layer
If Ribs > Ric then PBL top is reached
model surface

## Slide 33: A simple KPP scheme
If not reached, compute Ribs
between surface and next level up,
compare again to Ric
model surface
Finding PBL top h
~ depends on selected critical Ri (Ric)
Notes: NOT between layers 1 and 2. Between surface and layer 2.

## Slide 34: A simple KPP scheme
Keep going until
PBL top is found
h
model surface
Finding PBL top h
~ depends on selected critical Ri (Ric)
This is MRF’s PBL height
YSU uses this height as a first guess, and then
factors in a “thermal excess” at surface,
achieving a relatively higher h when PBL unstable
Notes: YSU uses this as first guess to PBL depth h. Then, it factors in a “thermal excess” and recomputes h, finding a higher value when PBL is unstable.

## Slide 35: A simple KPP scheme
Keep going until
PBL top is found
h
model surface
Finding PBL top h
~ depends on selected critical Ri (Ric)
Notes: YSU uses this as first guess to PBL depth h. Then, it factors in a “thermal excess” and recomputes h, finding a higher value when PBL is unstable.

## Slide 36: Km, Kh profile with height
Hong and Pan (1996)
YSU (diagnostic scheme) imposes this profile
based on diagnosed PBL height h
MYJ (prognostic scheme) tries to develop it
organically by predicting TKE

## Slide 37: Importance of PBL depth h
In KPP schemes, PBL depth h plays a crucial role, as it directly influences
  Mixing depth (obviously),
  Mixing magnitude, and
  Height of maximum mixing
    (located at z = h/3)
Ric largely determines h

## Slide 38: Selecting the critical Ric
We’re computing a bulk surface Ri, between some level z and the surface
Theoretical value: Ric = 0.25, but again this also depends on resolution and affected by averaging
Troen and Mahrt (1986) argued for Ric = 0.5 owing to low vertical resolution in PBL
MRF PBL scheme (Hong and Pan 1996), based on Troen and Mahrt (1986), also used Ric = 0.5
GFS PBL scheme (descended from MRF) adopted Ric = 0.25
YSU PBL (also descended from MRF) started with Ric = 0.5 (Hong et al. 2006). By 2010, it used Ric = 0.25 when stable, but Ric = 0 over land when surface layer is unstable (Hong 2010)
  The smaller Ric when unstable was adopted so that the PBL top would be diagnosed below the inversion, permitting explicit treatment of entrainment (see later)
Does this make a difference? (Yes, it can.)
Notes: Might be OK if Ric didn’t affect the forecasts, but of course it does.

## Slide 39
Standard YSU simulation at t = 49 (unstable surface layer)
In this situation, YSU uses Ric = 0.0 (not 0.25) for its first guess at h
Scheme determines PBL depth ~ 1 km
risfc.gs
Notes: YSUresults_at_time_49.pdf

## Slide 40
risfc.gs
Notes: When stable, may not matter all that much because mixing produced is so small.
Computed with risfc.gs

## Slide 41
The velocity scale ws also plays a key role, magnifying the mixing when surface
layer is unstable. (This term is more complex in YSU than in sister schemes.)
• Note diurnal variation of Km and ws. Shortly after sunrise, surface layer becomes
unstable, and ws (red curve) increases. At first, PBL depth h (blue curve PBLH)
is shallow, limiting the mixing (black curve).
• Later in the afternoon, surface layer becomes stable, and ws decreases quickly.
Mixing becomes small even though PBLH ostensibly remains deep.
• Note there are discontinuities in PBLH, caused by regime changes between
stable and unstable. (This is seen here because I used output every time step.)
Notes: Early in afternoon, ws grows quickly but PBLH is shallow, limiting the mixing magnitude and depth
Later, PBLH is deep but ws becomes small as sfc layer goes stable, becoming limiting factor on the mixing

## Slide 42: Augmenting local mixing with deep “nonlocal” mixing

## Slide 43: Reynolds-averaged q equation
• Km applies to momentum, Kh to heat
• That’s local mixing, between model
levels
Notes: Apply to theta eq instead. Will explain why – it’s for adding countergrad term, which MRF did not apply to momentum.
One of the neglected RHS terms is diabatic term

## Slide 44: Nonlocal mixing term added…
Adds a new term: for nonlocal mixing
Notes: Apply to theta eq instead. Will explain why – it’s for adding countergrad term, which MRF did not apply to momentum.

## Slide 45: Local vs. nonlocal mixing
Siebesma et al. (2007)
• The Km, Kh coefficients are attempting
to accomplish local mixing, as
indicated by the small eddies
• A convective boundary layer also
possesses deep thermals, which helps
make the layer well mixed
• Two approaches for enforcing nonlocal
mixing: the “countergradient” term
and the “mass flux” method
• MRF, YSU use countergradient
approach, forced by surface fluxes
• Mass flux or “EDMF” is a more recent
alternative
(ED = eddy diffusion = Km)
Lava lamp
Notes: Lava lamp

## Slide 46: Nonlocal mixing: MRF/YSU “countergradient” term
• Countergradient term is what makes this scheme nonlocal
• Term is generally parameterized based on surface fluxes
to capture effect of deep, penetrating thermals
• In MRF scheme, term applied only to temperature and water vapor
• In YSU, it is also applied to momentum
• This term is what effectively removes mixed layer vertical gradients
This accomplishes deep layer
(i.e., nonlocal) mixing
This does local mixing
Notes: Although TKE schemes try to do this too, many KPP schemes explicitly account for countergradient diffusion
\gamma_c > 0 for pot temp, increases tendency where dK/dz < 0 (PBL top) and decreases it where dK/dz > 0 (PBL bottom). Helps make less stable

## Slide 47: YSU with and without countergradient term
More recent versions
of MYNN have some
nonlocal mixing options
available
Notes: I added a namelist option to turn off countergradient terms in YSU

## Slide 48: Countergradient term history
The need to account for mixing associated with deep thermals to augment local mixing was recognized long ago (e.g., Priestley and Swinbank 1947; Deardorff 1966).
Troen and Mahrt (1986) included the countergradient term in the scheme that gave rise to the MRF, GFS, and YSU schemes.
The MRF and GFS (Hong and Pan 1996) apply the countergradient term to q and water vapor only.
Starting with Noh et al. (2003), YSU also applied it momentum.
  Troen and Mahrt (1986) explicitly excluded momentum from countergradient treatment
  Frech and Mahrt (1995), however, showed examples of well-mixed momentum profiles that countergradient momentum mixing can reproduce
  Still, Pleim (2007) notes “application of the countergradient term to other quantities has been problematic”.
YSU countergradient term was originally specified in terms of surface fluxes only.
  Wilson and Fovell’s (2018) revision to include fluxes at top of boundary layer (ysu_topdown_pblmix = 1) to handle fog cases. (This was a minor factor.)
Clearly, however, this is the term that permits YSU to remove the vertical shear in the mixed layer (last slide).
Notes: MYNN can do nonlocal momentum mixing but HRRR has not turned it on yet

## Slide 49: Aside: mass flux alternative to nonlocal mixing
The Troen-Mahrt approach to nonlocal mixing was (slightly rewritten):
The “mass flux” approach (Siebesma et al. 2007)
  Thermal updrafts are presumed to occupy a small area of the grid volume, with fractional area aup << 1.
  M is a mass flux = wupaup, where wup is updraft velocity
  Can obtain qup via an entraining plume model (Soares et al. 2004)
  Combined with eddy diffusion (ED), approach is called “EDMF”
  GFS-EDMF scheme based on GFS recently adopted for HWRF
Notes: Just the bare bones

## Slide 50: Entrainment into PBL
Siebesma et al. (2007)
• In addition to nonlocal mixing, air is also
being entrained into the PBL from
the free atmosphere above
• That’s also subgrid, and needs to be
parameterized, and there’s no one
way of doing that
Notes: Lava lamp

## Slide 51: PBL entrainment
Another MRF-YSU difference: YSU explicitly attempts to account for entrainment into the PBL from the free atmosphere.
  In the standard version, this term is also parameterized solely in terms of surface fluxes
entrainment term
PBL top flux, but made
inversely proportional
to surface flux
(z/h)3 function weighted towards
PBL top
ysu_topdown_pblmix = 1 makes
entrainment a function of PBL top
flux also. This was the key to improved
fog forecasts (Wilson and Fovell 2018).
Notes: Got here 2019
Epicycles?

## Slide 52: Aside on California fog…

## Slide 53
Wilson and Fovell (2018)
LES = Large Eddy Simulation
Key difference:
entrainment into PBL
ysu_topdown_pblmix=0
ysu_topdown_pblmix=1

## Slide 54: A quick peek at TKE-based (Mellor-Yamada) schemes
Including MYJ, MYNN2, MYNN3, QNSE, GBM
[WRF’s MYNN: Olson et al. (2019)]

## Slide 55: Recall from Part 1…
• Overbars were grid-averaged quantities (what the model is explicitly predicting)
• Primes indicate turbulent variations about those grid-averaged means
• We ignored molecular viscosity as insufficiently large
• We neglected the u’u’ term as small relative to u’w’ term (will reconsider that)
• We then developed a proxy for the u’w’ term based on eddy mixing Km
… but we need to backtrack…

## Slide 56: TKE and temperature variance
After defining TKE (velocity variance) as
  We saw…
We can also develop a prognostic equation for turbulent temperature variance and …
related to shear
related to vertical heat flux
dissipation/
other terms
Notes: Not jumping just yet to develop proxies for these eddy covariances

## Slide 57
We wind up with equations for a large set of eddy covariances in the Mellor and
Yamada “Level 3” model, which contain a sizable set of parameters in need of values
[Notation shift… TKE e = q2/2, and u = u’, etc.]
What sets some TKE schemes apart is which terms retained and parameter values chosen.
MYNN2 is a further simplified version of MYNN3.
Jahn et al. (2017)
MYNN3 scheme
Notes: First eq is \bar{u’u’}. In eq (12), their numbering, term 3 in bracket looks a little like our original proxy, but this is much much more complicated
A real mess of algebraic manipulation
Actually Jahn et al’s second 2017 paper

## Slide 58: How parameters vary among related schemes
Jahn et al. (2017)
MYJ and MYNN3 in WRF
NOTE: MYNN has changed a lot since WRF V3.5.1
Notes: Lots of terms means lots of tunable parameters

## Slide 59
Observations from ~60 radiosonde locations
HRRR MYNN2 forecasts at analysis time (00 h forecast)
HRRR MYNN2 forecasts at hours 23 and 24
Fovell and Gallagher (2020)
Evaluating HRRR wind speed profiles
near the ground
contaminated
observations
contaminated
observations
We also evaluated
temperature profiles
in the PBL
Notes: Remind why this stuff can matter

## Slide 60: PBL and surface layer schemes
PBL and surface layer (not LSM) schemes are often paired. Some combinations are optimized, and others do not work.
Names of eddy mixing coefficients vary among schemes
bl_pbl_physics (incomplete list) | Scheme name | sf_sfclay_physics (bold = default) | Km | Kh
1 [Hong 2010] | YSU (KPP) | 1, 91 | dku3d | dkt3d
2 [Janjic 1994] | MYJ (TKE) | 2 | -- | exch_h
4 [Sukoriansky et al. 2005] | QNSE (TKE) | 4 | exch_m | exch_h
5 [Olson et al. 2019] | MYNN2 (TKE) | 1, 2, 5, 91 | exch_m | exch_h
6 [Olson et al. 2019] | MYNN3 (TKE) | 1, 2, 5, 91 | exch_m | exch_h
7 [Pleim 2007] | ACM2 (KPP) | 1, 7, 91 | -- | exch_h
11 [Shin and Hong 2015] | Shin-Hong (KPP) | 1, 91 | -- | exch_h
99 [Hong and Pan 1996] | MRF (KPP) | 1, 91 | dku3d | dkt3d
Surface layer scheme 91 is the old version of scheme 1 (Jimenez et al. 2012). MYNN surface layer: Olson et al. (2021)
Notes: Here 2022

## Slide 61: Extra info
I showed previously how surface roughnesses were defined in LANDUSE.TBL. When the Noah LSM is used, however, those are overridden by values defined in VEGPARM.TBL.
  Roughness values are saved in wrfout files as both Z0 and ZNT.
In VEGPARM.TBL, landuse categories are assigned max and min roughness values, Z0MAX and Z0MIN. The Noah LSM (sf_surface_physics=2) imposes a seasonal cycle* with these values as bounds, and does this during the first time step (after 1st wrfout write).
  As a consequence, Z0 & ZNT values written to wrfout for the first time step (at model start) are likely to be incorrect
*See, for example, Fig. 8 of Cao and Fovell (2018)