## Slide 1: Supercell storms: In-class demo
ATM 419/563
Spring 2024
Fovell
© Copyright 2024 Robert Fovell, Univ. at Albany, SUNY, rfovell@albany.edu
This demo is configured for head.arcc/batch system

## Slide 2: Goals
Start idealized WRF 3D run to simulate a splitting supercell thunderstorm (in-class demo)
Submit WRF job to the batch system
Review supercell storm structure and behavior (while model runs)
Analyze demo simulation using Python

## Slide 3: Setup [see script]
Create a folder called SUPERCELL in your lab space
  $ lab
  $ mkdir SUPERCELL
  $ cd SUPERCELL
Copy /network/rit/lab/atm419lab/SUPERCELL/SETUP.TAR there and unpack
  $ cp $LAB/SUPERCELL/SETUP.TAR .
  $ tar –xvf SETUP.TAR
  Files included: make_all_links.sh, namelist.input, input_sounding, read_wrfinput.py, submit_wrf, plot_SUPERCELL.ipynb
Pre-configured for a 1-h run in a 168 km by 168 km domain at 2 km horizontal grid spacing
  Initial sounding derived from Weisman and Klemp (1982)
  “quarter-circle” wind profile favors storm splitting and right-mover
  Purdue-Lin microphysics (mp_physics = 2)
  Time step 12 seconds
  History output every 5 min
Notes: read_wrfinput.py
WK sounding was slightly modified from original

## Slide 4: Outline
ideal.exe program reads in input_sounding and namelist.input and creates wrfinput_d01, the input file for the WRF model
wrf.exe program reads in namelist.input and wrfinput_d01 and creates output file(s) called wrfout_d01…
Most file extensions are meaningless in Unix.

## Slide 5: input_sounding
1000.0000 300.0000 14.000000
10.0000 300.0061 14.000000 -8.0998 -4.9419
35.0000 300.0291 14.000000 -8.0976 -4.7968
100.0000 300.1083 14.000000 -8.0802 -4.4199
200.0000 300.2575 14.000000 -8.0208 -3.8426
300.0000 300.4275 14.000000 -7.9222 -3.2706
400.0000 300.6125 14.000000 -7.7848 -2.7067
500.0000 300.8095 14.000000 -7.6092 -2.1535
600.0000 301.0167 14.000000 -7.3963 -1.6136
700.0000 301.2327 14.000000 -7.1470 -1.0894
800.0000 301.4566 14.000000 -6.8626 -0.5835
900.0000 301.6877 14.000000 -6.5442 -0.0982
[…]
surface pressure (mb) surface theta (K) surface vapor (g/kg)
height (m) theta (K) water vapor (g/kg) u (m/s) v (m/s)
[For information. You do not need to edit this file at this time.]
[These data will be interpolated onto the WRF vertical grid, yet to be specified]
Notes: Got to here 2022

## Slide 6
Weisman and Klemp (1982)
Boundary layer mixing
ratio is 14 g/kg in
input_sounding
Copies of papers cited in this
course available on class page

## Slide 7: Hodograph (see input_sounding)
2 km AGL
surface
7 km AGL

## Slide 8: Part of namelist.input
&time_control
run_days = 0,
run_hours = 0,
run_minutes = 60,
run_seconds = 0,
start_year = 0001,
start_month = 01,
start_day = 01,
start_hour = 00,
start_minute = 00,
start_second = 00,
end_year = 0001,
end_month = 01,
end_day = 01,
end_hour = 00,
end_minute = 120,
end_second = 00,
history_interval = 5,
frames_per_outfile = 1000,
&domains
time_step = 6,
time_step_fract_num = 0,
time_step_fract_den = 1,
max_dom = 1,
s_we = 1,
e_we = 60,
s_sn = 1,
e_sn = 60,
s_vert = 1,
e_vert = 41,
dx = 2000,
dy = 2000,
ztop = 20000,
Run for 60 min with 5 min outputs
6 second time step
60 x 60 grid points
41 model levels
2000 m horizontal grid spacing
Model top at 20000 m
[For information. You do not need to edit this file at this time.]

## Slide 9: Using the batch system
Look at the file submit_wrf:
#!/bin/bash
# Job name:
#SBATCH --job-name=atm419wrf
#SBATCH -n 6
#SBATCH -N 1
#SBATCH --mem=131072
#SBATCH -o sbatch.out
#SBATCH -e sbatch.err.out
[…]
echo "running WRF"
srun -N 1 -n 6 --mpi=pmix -o wrf.srun.out ./wrf.exe
Change to your name [optional]
Requests 6 cpus on 1 node
Where run time errors might be reported
This runs the model.
The –N and –n values must match
those provided at the top
[For information. You do not need to edit this file at this time.]

## Slide 10: Initialize and run model
sh make_all_links.sh
srun ideal.exe
  Ignore the ”OpenFabrics” warning
  To see if the job worked: type trsl, which stands for “tail –f rsl.out.0000”. Look for wrf: SUCCESS COMPLETE IDEAL INIT
  Type CTRL-c to break free.
What is the lowest scalar model level height? [see next slide]
  dopython
  python read_wrfinput.py wrfinput_d01
Submit your batch job:
  $ sbatch submit_wrf
Check on your job
  $ myjobs
A configuration file. Not interchangeable
between real and ideal experiments, and
among ideal experiments.
Notes: Lowest scalar height: 285 m. Not uncommon for cloud model simulations. Not even trying to capture PBL properly. There is no PBL.
dopython executes script in extras.csh or extras.bash to set up more modern envirionment than default on headnode

## Slide 11
$ python read_wrfinput.py wrfinput_d01
The filename is wrfinput_d01
terrain height 0.0 meters
----------------------------------------------------------------
model level 01 W height 0.00 S height 284.70
model level 02 W height 569.41 S height 850.65
model level 03 W height 1131.89 S height 1409.49
model level 04 W height 1687.09 S height 1960.53
model level 05 W height 2233.98 S height 2503.62
model level 06 W height 2773.26 S height 3039.37
model level 07 W height 3305.48 S height 3568.30
model level 08 W height 3831.11 S height 4090.82
model level 09 W height 4350.53 S height 4607.30
model level 10 W height 4864.07 S height 5118.05
model level 11 W height 5372.03 S height 5623.34
model level 12 W height 5874.66 S height 6123.44
model level 13 W height 6372.21 S height 6618.55
model level 14 W height 6864.88 S height 7108.88
model level 15 W height 7352.88 S height 7594.63
model level 16 W height 7836.39 S height 8075.98
model level 17 W height 8315.58 S height 8553.11
model level 18 W height 8790.63 S height 9026.17
model level 19 W height 9261.71 S height 9495.35
model level 20 W height 9728.99 S height 9960.81
model level 21 W height 10192.62 S height 10422.71
model level 22 W height 10652.79 S height 10881.23
model level 23 W height 11109.67 S height 11336.55
model level 24 W height 11563.44 S height 11788.86
model level 25 W height 12014.27 S height 12240.10
model level 26 W height 12465.92 S height 12693.85
model level 27 W height 12921.77 S height 13151.99
model level 28 W height 13382.21 S height 13614.90
model level 29 W height 13847.59 S height 14082.97
model level 30 W height 14318.35 S height 14556.67
model level 31 W height 14794.98 S height 15036.48
model level 32 W height 15277.99 S height 15522.98
model level 33 W height 15767.98 S height 16016.79
model level 34 W height 16265.60 S height 16518.60
model level 35 W height 16771.61 S height 17029.22
model level 36 W height 17286.83 S height 17549.54
model level 37 W height 17812.24 S height 18080.58
[more]
As we will see, vertical velocity (W)
and scalars (S) are defined at
different physical heights.
The lowest W height is zero (ground)
The lowest S height is 284.7 m
The model top is a W height, located
at 20040.07 m

## Slide 12: As the model runs…
The model writes output to four kinds of files (in addition to wrfout…)
  rsl.out.XXXX (numbered 0000 to 1-n, n =number of cores requested; we requested 6 cores)
  rsl.error.XXXX (numbered as above; not really error)
  sbatch.out (timing info when job completed)
  sbatch.err.out (hopefully empty file most of time!)
As the model runs, you can monitor progress with
  $ trsl
  [This is an alias for tail -f rsl.out.0000]
  [type ‘CTRL-c’ to quit/escape from this]
  Look for SUCCESS COMPLETE WRF

## Slide 13: Supercell structure and behavior

## Slide 14: Supercells
Characterized by rotating updrafts (vertical velocity and vertical vorticity co-located)
  Mesocyclone and “hook echo”
Develop in environments with large vertical wind shear
Evolve from ordinary cells by “splitting” into “left-movers” and “right-movers”
Clockwise directional vertical wind shear favors right-movers

## Slide 15
Split
L mover weaker
R mover turns right
R mover hook
Purple = hail
Notes: 24apr2006_split_dfx_n0r01.GIF

## Slide 16: Splitting storms
Wilhelmson and Klemp (1981)

## Slide 17: Shear-induced horizontal vorticity

## Slide 18: Dynamics of storm splitting
• Lifting of vortex tubes by updraft
creates counter-rotating vortices
(vertical vorticity)
• Low perturbation pressure develops
that establishes new updrafts on
flanks of original storm
• New cells are rotational: CCW or CW
• Old cell dies, giving appearance of
split
• Actually, precipitation does NOT
cause the updraft split!
Notes: Bottom panel appears to show the new split cells are NOT rotating but instead have counterrotating vortices on THEIR sides as well. That is not consistent with our modern understanding

## Slide 19: Original updraft
Updraft is *not* rotating

## Slide 20: Counter-rotating vortices
Cyclostrophic lows

## Slide 21: New storms form on flanks
New updrafts ARE rotating

## Slide 22: Old cell decays

## Slide 23
> 65+ dBZ
(hail or airborne debris)
hook echo
reflectivity

## Slide 24
radial velocity

## Slide 25
Supercell conceptual
model

## Slide 26
Storm-scale fronts
T = tornado location

## Slide 27
mesocyclone
meso = Gk., middle

## Slide 28
Updraft velocities can easily
exceed 100 mph

## Slide 29
RFD = rear flank downdraft
FFD = forward flank downdraft

## Slide 30
warm, moist air
lifted into updraft

## Slide 31: Supercell storm structure
Plan view at surface
UD = updraft
FFD = forward flank downdraft
RFD = rear flank downdraft
Gust front
Hook echo
Dot ~ tornado location
Lemon and Doswell (1979)

## Slide 32: [After simulation finishes…]

## Slide 33: Visualizing the supercell simulation with WRF-Python

## Slide 34: The wrfout output file
Your WRF output file is called wrfout_d01_0001-01-01_00:00:00. It contains 13 output times, every 5 min for 1 hour (including the initial time)
  Because this was a short simulation that did not generate much output, we allowed WRF to write all output fields and times into a single file
  In more demanding applications, we might write fields at each output time into a separate file

## Slide 35: Launch ARCC’s jupyter
https://jupyterlab.its.albany.edu/hub/login
If presented with a drop down menu, select batch – 1 core, 4 GB, 8 hours
Click on your LAB link in your home directory
  You may need to click on “Last modified” button at upper right twice
Click on your SUPERCELL directory
Launch the notebook plot_SUPERCELL.ipynb

## Slide 36
X,Y axes labeled as grid points, not distance in km. Should change that.
Horizontal wind speed (colored and barbs, m/s), column max vertical velocity (white contours)

## Slide 37
Notes: Can improve by removing redundant colorbars and unneeded labels, etc.

## Slide 38
Horizontal wind speed (colored), vertical velocity (white contours), theta (black contours)

## Slide 39: Where to go from here?

## Slide 40
Weisman and Klemp (1982)
Weisman and Klemp (1982) varied the sounding’s
buoyancy B (= CAPE) by changing the mixing ratio
profile (qv0), and varied the wind profile shear Us,
investigating the effect of CAPE and shear on
storm mode: supercell (“split storm”) vs. multicell
(“secondary storm”)

## Slide 41: [end]
Notes: “courier du bois” = runner of the woods