## Slide 1: Thunderstorm case demonstration and cumulus ensemble
ATM 419/563
Spring 2024
Fovell
© Copyright 2024 Robert Fovell, Univ. at Albany, SUNY, rfovell@albany.edu
SNOW cluster version
Cumulus ensemble completion by start of class Thursday, April 4

## Slide 2: Outline
Create and position an outer domain + nest
  D1 = Domain 1 (12 km)
  D2 = Domain 2 (4 km nest… 3:1 ratio standard)
Make a 12 h simulation using 1 domain initialized with GFS and using the Kain-Fritsch cumulus scheme
  Our common control run
Compare to simulation made with 2 domains without cumulus in inner nest; i.e.,
  D1 uses a cumulus parameterization and a microphysics scheme
  D2 relies on microphysics only
Contribute to a class cumulus scheme ensemble with some variation of microphysics
Please also refer to WRF REAL CHECKLIST

## Slide 3: Resources
$LAB/SCRIPTS/WRF_REAL_SETUP_SNOW.TAR
$LAB/TSTORM/plot_WRF_TSTORM.ipynb
  Output files created like
    TCU01_planview_Fovell.png
    TCU01_timeseries_Fovell.png
    TCU01_Fovell_precip.csv
Script: TSTORM_demonstration.pdf
WRF REAL CHECKLIST from class web page

## Slide 4: Objective
By completion of this demonstration, we will have covered:
  how and why some parameterizations work (and fail),
  what to check when creating a domain,
  how to create a parent domain with nests,
  how to initialize WRF using different data sets,
  how to visualize model output using Python,
  how parameterizations for subgrid-scale clouds (cumulus schemes) can vary and compete with microphysics,
Soon, we will also cover:
  how to verify forecasts against surface observations,
  how the model is integrated in time and discretized in space,
  how to recognize, diagnose, and mitigate numerical difficulties,
  how to perturb forecasts and modify model default levels
Notes: As a result of the course to date…

## Slide 5
1200Z 31 March 2022

## Slide 6
1800Z 31 March 2022

## Slide 7
0000Z 1 April 2022
SQUALL

## Slide 8
https://www2.mmm.ucar.edu/imagearchive/
1155Z 31 March 2022

## Slide 9
1755Z 31 March 2022
Pre-frontal squall line forms

## Slide 10
2325Z 31 March 2022
Trailing stratiform region now apparent behind squall. Convection also along cold front

## Slide 11
“TRUTH” – 2 domains, microphysics only in D2 (no cumulus) – forecast hour 11
4 km ∆x
Cumulus OFF
Wind barbs every 6 gridpoints
Notes: Cold front maybe too far east.

## Slide 12
TCU01 – 1 domain, cu_physics=1 [our control run] - forecast hour 11
12 km ∆x
Cumulus ON
Wind barbs every 2 gridpoints
Notes: Convec along cold front seen in CU

## Slide 13
“TRUTH” – west east cross-section at 42N – forecast hour 11
Modified version of plot_vertical_cross_section_wrfpython.ipynb
4 km ∆x
Cumulus OFF
More realistic --> more correct?????

## Slide 14
TCU01 – west east cross-section across Albany – forecast hour 11 [our control run]
Made with plot_WRF_TSTORM.ipynb
12 km ∆x
Cumulus ON
Notes: We’re 42.75N

## Slide 15
Total precipitation in a defined subdomain

## Slide 17: Setup
(see also script)
[Ungrib and Geogrid steps can be done simultaneously…]

## Slide 18
&geogrid
parent_id = 1, 1,
parent_grid_ratio = 1, 3,
i_parent_start = 1, 22,
j_parent_start = 1, 32,
s_we = 1, 1,
e_we = 115, 166,
s_sn = 1, 1,
e_sn = 100, 100,
geog_data_res ='default', 'default',
dx = 12000.,
dy = 12000.,
&share
wrf_core = 'ARW',
max_dom = 2,
start_date ='2022-03-31_12:00:00', '2022-03-31_12:00:00'
end_date = '2022-04-01_00:00:00', '2022-04-01_00:00:00'
interval_seconds = 3600,
namelist.wps
NOW the second column – where it appears -- matters
Same start/end times for both domains
grey: never altered
UNGRIB STEP
Notes: Grey = these are never altered.
Our WRF core is ARW

## Slide 19: Ungrib step
cp Vtable.GFS Vtable
link_grib.csh $LAB/DATA/GFS_2022033112/gfs* .
sbatch –p snow submit_ungrib
[you may need to wait for job to start]
tail –f ungrib.log
“*** Successful completion of program ungrib.exe ***”. THIS TAKES TIME.
[Consider opening TWO connections to headnode7, so you can do the
ungrib and geogrid steps simultaneously]
{see also script. Follow real-data checklist.}

## Slide 20: Geogrid step
2 domains maximum
D1: 115 e_we x 100 e_sn points, 12 km resolution grid spacing
D2: 166 e_we x 100 e_sn points, 4 km resolution grid spacing
  D2 lower left corner positioned at (22, 32) = (i_parent_start, j_parent_start) within D1 [see slide 22]
  D2:D1 grid ratio will be 3:1 (standard)
Lambert projection
  Reference latitude: 42.6˚
  Lambert true latitudes: both 42.6˚
  Reference and standard longitudes: -76˚
Edit namelist.wps as needed
Inspect domain using ncl plotgrids.ncl (don’t skip this; see slide 22)
Execute geogrid.exe somehow [see slide 25]
Make sure you have two new files: geo_em.d01.nc, geo_em.d02.nc
Use ncview on geo_em.d01.nc to check out max and min map factors (MAPFAC_M)
{see also script. Follow real-data checklist.}
[Consider opening TWO connections to headnode7, so you can do the
ungrib and geogrid steps simultaneously]
Notes: Max map factor 1.00459, min 1.0

## Slide 21
&geogrid
parent_id = 1, 1,
parent_grid_ratio = 1, 3,
i_parent_start = 1, 22,
j_parent_start = 1, 32,
s_we = 1, 1,
e_we = 115, 166,
s_sn = 1, 1,
e_sn = 100, 100,
geog_data_res ='default', 'default',
dx = 12000.,
dy = 12000.,
&share
wrf_core = 'ARW',
max_dom = 2,
start_date = '2022-03-31_12:00:00', '2022-03-31_12:00:00'
end_date = '2022-04-01_00:00:00', '2022-04-01_00:00:00'
interval_seconds = 3600,
Controls nest grid spacing
(D2 = D1/3)
[3:1 ratio is standard]
Controls location
(lower left corner) in parent
[see next slide]
namelist.wps
D1’s grid spacing ONLY
NOW the second column – where it appears -- matters
Same start/end times for both domains
grey: never altered
Notes: Grey = these are never altered.
Our WRF core is ARW

## Slide 22
∆x = 12 km
∆x = 4 km
Output from
ncl plotgrids.ncl
Make sure your domain looks
like this before moving on!
(22,32)

## Slide 23
Output from plot_WRF_domain.ipynb
Make sure your domain looks like this before moving on!

## Slide 24
Terrain of D1
Output from plot_WRF_terrain.ipynb
plt.Normalize was altered for this plot

## Slide 25: Running geogrid.exe
The geogrid program can take some time, especially when generating large nests.
However, geogrid is also MPI-aware (all WPS/WRF programs are, except ungrib.exe and tc.exe)
Two options:
  (1) Ask for multiple cpus with srun. Example:
    srun –p snow –n 8 geogrid.exe
  (2) Submit a batch job (submit_geogrid provided)
    sbatch –p snow submit_geogrid
    tail –f geogrid.srun.out
Notes: Mapfacs 1 to 1.00459

## Slide 26: Metgrid step [after ungrib AND geogrid are finished]
sbatch –p snow submit_metgrid
tail –f metgrid.log.0000
“*** Successful completion of program metgrid.exe **”
Select one of the met_em.d* files generated, and dump the header (ncdump –h) to look for num_metgrid_levels, num_st_layers, num_sm_layers

## Slide 27
&ungrib
out_format = 'WPS',
prefix = 'FILE',
/
&metgrid
fg_name = 'FILE',
io_form_metgrid = 2,
/
constants_name = './TAVGSFC',
Typical for ungrib outputs
== metgrid inputs to be
named “FILE”. You should
change this if manipulating
more than one data source
simultaneously
If a “constants file” is needed
[e.g., landmask or other
temporally invariant info]
it would be defined and placed ABOVE the / line
namelist.wps
Relevant to ungrib and metgrid steps
grey: very rarely altered
Notes: Grey = these are never altered.
Our WRF core is ARW

## Slide 28: Real and WRF steps
Edit namelist.input, as described in script
Make sure
  Start/end times, interval_seconds match namelist.wps
  num_metgrid_levels, num_metgrid_soil_levels are set correctly
  Domain size and resolution and nest location set as in namelist.wps
  max_dom = 1 for this demo
  Model physics and time step set as in script

## Slide 29
&time_control
run_days = 0,
run_hours = 12,
run_minutes = 0,
run_seconds = 0,
start_year = 2022, 2022,
start_month = 03, 03,
start_day = 31, 31,
start_hour = 12, 12,
start_minute = 00, 00,
start_second = 00, 00,
end_year = 2022, 2022,
end_month = 04, 04,
end_day = 01, 01,
end_hour = 00, 00,
end_minute = 00, 00,
end_second = 00, 00,
interval_seconds = 3600,
input_from_file = .true., .true.,
history_interval = 60, 60,
frames_per_outfile = 99999, 99999,
namelist.input
NOW the second column – where it appears -- matters
Notes: Check the stuff in red. All will need to change.

## Slide 30
&domains
time_step = 30,
time_step_fract_num = 0,
time_step_fract_den = 1,
max_dom = 1,
e_we = 115, 166,
e_sn = 100, 100,
e_vert = 57, 57,
p_top_requested = 5000,
num_metgrid_levels = ??,
num_metgrid_soil_levels = ?,
dx = 12000., 4000.,
dy = 12000., 4000.,
grid_id = 1, 2,
parent_id = 0, 1,
i_parent_start = 1, 22,
j_parent_start = 1, 32,
parent_grid_ratio = 1, 3,
parent_time_step_ratio = 1, 3,
namelist.input
MAKE SURE INFO MATCHES namelist.wps!
D2 has 1/3 the grid spacing of D1, and will use 1/3 the time step
For D1
1 domain (for demo)
Our choice but need
to be same for each domain
Notes: Need to directly specify D2 grid spacing (4000 m) and indirectly (through parent_grid_ratio = 3)

## Slide 31: Run real and WRF
sbatch -p snow submit_real
tail -f rsl.out.0000: “real_em: SUCCESS COMPLETE REAL_EM INIT”
sbatch -p snow submit_wrf
tail -f rsl.out.0000: “real_em: SUCCESS COMPLETE WRF”
This will take awhile and may not finish in today’s class. But, once you’re done…

## Slide 32: Visualize output with plot_WRF_TSTORM.ipynb
Cell #3
############################################################################ set your surname and scheme name
###########################################################################
surname = 'Fovell'
scheme = 'TCU01'
print(" Hi ",surname,"! Your scheme is ",scheme)
You’ll modify the red lines for your ensemble contribution
[slides 38-41]

## Slide 33
Cell #5

## Slide 34
Cell #7
Barbs every
4 gridpts

## Slide 35
Cell #8
Wind barbs every 2 gridpoints

## Slide 36
Cell #9

## Slide 37
Cell 10

## Slide 38: Cumulus ensemble
Modify namelist.input as needed [following slides]
Rerun real.exe and wrf.exe
Edit Cell #3 in plot_WRF_TSTORM.ipynb for your surname and your schemename
cp *schemename* $LAB/TSTORM_ensemble/.
Cumulus ensemble completion by start of class Thursday, April 4

## Slide 39
Last Name | Ugrad or Grad | name | cu_physics | scheme | mp_physics
Fovell | [class] | TCU01 | 1 | KF | 8
Belkin | Ugrad | TCU02 | 2 | BMJ | 8
Birnbaum | Ugrad | TCU03 | 3 | GF | 8
Boschulte | Ugrad | TCU05 | 5 | G3 | 8
Castro | Ugrad | TCU06 | 6 | Tiedtke | 8
Crespo | Ugrad | TCU10 | 10 | KF-CuP | 8
Ehresman | Ugrad | TCU11 | 11 | MS-KF | 8
Farash | Ugrad | TCU14 | 14 | KSAS | 8
Geiger | Ugrad | TCU16 | 16 | New Tiedtke | 8
Gilberti | Ugrad | TCU93 | 93 | GD | 8
McGuire | Ugrad | TCU94 | 94 | HWRF SAS | 8
Megello | Ugrad | TCU95 | 95 | Old SAS | 8
O'Brien | Ugrad | TCU96 | 96 | NSAS | 8
Olsen | Ugrad | TCU99 | 99 | Old KF | 8
Table #1 of 3
Members using Thompson
microphysics (mp=8)
mp_physics = 8
cu_physics = [as noted above]

## Slide 40
Last Name | Ugrad or Grad | name | cu_physics | scheme | mp_physics
Podmayersky | Ugrad | MCU01 | 1 | KF | 10
Prego | Ugrad | MCU02 | 2 | BMJ | 10
Walter | Ugrad | MCU03 | 3 | GF | 10
White | Ugrad | MCU05 | 5 | G3 | 10
Williams | Ugrad | MCU06 | 6 | Tiedtke | 10
Zywiczynski | Ugrad | MCU10 | 10 | KF-CuP | 10
Alwang | Grad | MCU11 | 11 | MS-KF | 10
Czech | Grad | MCU14 | 14 | KSAS | 10
De Castro | Grad | MCU16 | 16 | New Tiedtke | 10
Desousa | Grad | MCU93 | 93 | GD | 10
Ellingworth | Grad | MCU94 | 94 | HWRF SAS | 10
Evans | Grad | MCU95 | 95 | Old SAS | 10
Glasser | Grad | MCU96 | 96 | NSAS | 10
Hernandez | Grad | MCU99 | 99 | Old KF | 10
Table #2 of 3
Members using Morrison
microphysics (mp=10)
mp_physics = 10
cu_physics = [as noted above]

## Slide 41
Last Name | Ugrad or Grad | name | cu_physics | scheme | mp_physics
Hojeily | Grad | WCU01 | 1 | KF | 3
Khadka | Grad | WCU06 | 6 | Tiedtke | 3
Oppong | Grad | WCU16 | 16 | New Tiedtke | 3
Sinnenberg | Grad | TNOCU | 0 | no cumulus | 8
Smith | Grad | MNOCU | 0 | no cumulus | 10
Table #2 of 3
Special cases
mp_physics = [as noted above]
cu_physics = [as noted above]

## Slide 42: [end]