## Slide 1: Real-data WRF: Forecast verification (Boulder windstorm Part 3)
ATM 419/563
Spring 2024
Fovell
© Copyright 2024 Robert Fovell, Univ. at Albany, SUNY, rfovell@albany.edu

## Slide 2: Overview
Surface station comparison: WRF forecasts v. observations
Data sources:
  Your WRF simulation of the Boulder windstorm of December 2021
  Surface observations from the NOAA MADIS archive
  Focus on near-surface temperature and wind speed for this example
Tools:
  UPP (Unified Post Processor - unipost): converts WRF output to GRIB format for MET
  MET (Model Evaluation Tools): performs comparisons, computes statistics
  Python for charts and maps, with topo maps from Google
Goal:
  Assess how good WRF forecast skill is, and whether we need to reevaluate model configuration
  Consider the question: are all surface observations created equal?

## Slide 3: Verification for your final project would involve
Obtaining observations from MADIS and preparing them
Running UPP on your WRF model output
Running MET
Visualizing your results
Understanding limitations of both the model and the observations
Using the verification to evaluate and improve your experiment

## Slide 4: Surface stations [keep in mind WRF forecasts “2 m T” and “10 m wind”]
ASOS
  Primarily at airports
  Sonic anemometers, nominally mounted at 10 m AGL, usually flat and well-exposed (but not always)
AWOS
  Older installations, often non-sonic, at smaller and lesser used airports; many commingled with ASOS in MADIS
RAWS
  US Forest Service and other agencies, primarily sited on mountain slopes, often obstructed by trees
  Propeller or cup/vane anemometers nominally mounted at 6.1 m AGL, non-aspirated thermistors
MESOWEST
  An eclectic mix of stations, including many public utilities and highway and railroad mesonets
  Public utility mesonets often use propeller anemometers mounted at various heights, including 6.1 m AGL
APRSWXNET
  A real polyglot mix of citizen- and corporate-owned weather stations, many in people’s backyards
OTHER
  Include agriculture stations, avalanche stations, hydromet stations, etc. Some anemometers at 2 m AGL
There are differences in instrument type (sonic vs. non-sonic anemometer), mounting height, instrument
characteristics (aspirated vs. non-aspirated), characteristic placement and exposure – and reason for placement

## Slide 5: Boulder windstorm simulation
Verification using MET against observations collected in Colorado and extracted from the NOAA MADIS public database
  Our domain extended beyond Colorado’s state borders
Our MET scripts compare a station to the nearest model grid point
  We could also interpolate model fields to station’s lat/lon location
  We’re also not filtering for elevation differences between model and station
We have hourly output. MET will find observations valid for as close to the top-of-hour that are available
  At an extreme, observations may be up to 30 min before or after model valid time. There are other options available
We start by verifying against all available observations. Follow script.

## Slide 6: Network- and station- averaged results
Using ALL available stations

## Slide 7
MET6_ALL.sh
OBS_base=$MYLAB/DATA/MADIS/DEC2021_BOULDER_V2/
ALL STATIONS in COLORADO available in MADIS
Up to 1050 stations depending on variable and time
Network averages
T: cold bias
Td: wet bias
RH: high bias
Wind: very overpredicted,
especially at peak
RED = observations
BLACK = forecast
N = avg number of stations available
Notes: How do you overpredict the wind during a windstorm?

## Slide 8
Each dot is a
station averaged
over 13 h
ALL
Is there
skill here?
The bias is
biased!
Some of these
obs are outliers
and probably bad
but don’t change
basic result
 Obs are dirty
Bias = forecast
minus obs

## Slide 9
ALL
Star =
Boulder
Marker color:
red + bias
blue – bias
size ∝ bias size
MADIS state
filtering is
imperfect

## Slide 10
ALL
Star =
Boulder
Marker color:
red + bias
blue – bias
size ∝ bias size
MADIS state
filtering is
imperfect

## Slide 11: Task: further evaluate this simulation
See ”MET assignment” on class web page

## Slide 12: [end]